Inspection Check List for Amateur-Built Aircraft Inspection

Ask your local FAA Inspector or Designated Airworthiness Representative (DAR) what He/She uses in your area. Always contact your local FAA office for official information.

Finally, this list is not all inclusive, but generic in nature. A combination of Regulatory as well as Best Practice items are included.

General

Builder: _______________________________________ Model _________ S/N __________

Date of Inspection__________ Inspector _______________________________

Regulatory Prerequisites, Best Practices & Placards

Satisfactory Unsatisfactory Item

____ _____ 1. Meets 51% rule, has invoices, plans, pictures and building records

____ _____ 2. Presents notarized statement FAA Form Eligibility Statement

____ _____ 3. Presents FAA Form 8130-6 Application for A/W Certificate properly filled out

____ _____ 4. ID data plate is fireproof (steel), has Builder's name, model, serial number.

____ _____ 5. ID data plate is installed in proper external location per FAR 45. 11(a).

____ _____ 6. N-Numbers installed, block letters, 3" proper location per FAR 45.25, or 12 inch, if a/c has cruise speed over 180 Knots CAS.

____ _____ 7. Word Experimental Displayed, 2" min size, proper location per FAR 45.23(b).

____ _____ 8. Passenger warning placard (not required for single place) "..does not meet U.S. safety standards for certified aircraft..."

____ _____ 9. Registration certificate available in aircraft. (NOT pink slip!)

____ _____ 10. Builder makes statement in logbook that aircraft has been inspected

____ _____ 11. A/C Weight and balance done, and shows within designer's limits.

FAR 91.9 Placards

____ _____ 12. ALL controls - flight and engine, marked as to use.

____ _____ 13. Markings for :

____ ______Throttle- open-closed

____ _____ Carb Heat- pull on

____  _____ Flaps- Up- Down, Degrees/Inches Take Off Setting Marked

____  _____ Trim Tab- Nose Up, Nose Down, Take Off setting

____  _____ Trim Tab- rudder left, rudder right, neutral

____ _____ Mixture- Push rich

____ _____ Fuel On-Off levers

____ _____ Fuel quantity and type marked on or near each cap

____ _____ Emergency placards, Gear extension, etc.

Cockpit interior

_____ _____ Seat Belts function, and angle is slightly rearward

_____ _____ Shoulder harness function, and angle is -5 to + 30 degrees

_____ _____ Seat Belt Anchor Points firm, no interference

_____ _____ Shoulder Harness Anchor Points firm, no interference

_____ _____ Seats and seat tracks o.k., stops on aft of rails

_____ _____ Canopy access from outside for emergencies & Placard

Instruments and required equipment

___ ____ ___14. ELT meeting TSO-C91A properly installed, with remote switch and battery date current and recorded in aircraft records

_____ _____ 15. Fuel gauge each tank, has been calibrated and calibration in records showing unusable fuel

_____ _____ 16. VFR Day requirements: * Note: All instruments should be marked with green/red line ranges

_____ _____ Altimeter

_____  ____ Airspeed indicator

_____ ____ Tachometer

_____  ____ Oil Pressure

_____ ____ Oil Temperature

_____ ____ Compass

_____ ____ For retract gear aircraft, indicator of up/down gear

_____ ____ Basic engine temp and pressure instrument calibration and function

____ ______ 17. VFR Night Requirements- Day VFR plus:

_____  ____ Position Lights meet FAA Standard

_____  ____ Anti-collision strobes/rotating beacon which meets FAA standards

_____ ____ Spare fuses cockpit in flight access required for IFR applications

_____ ____ Electrical energy sufficient for duration of aircraft range, plus  reserve

____ _____ 18. IFR Requirements Day & Night VFR, plus:

_____ ____ Working two-way radio (See Checklist explanations Page)

_____ ____ Gyroscopic rate of turn indicator (Turn & Bank or Turn Coordinator)

_____ ____ Slip / Skid indicator

_____ ____Sensitive altimeter

_____ ____ Artificial horizon

_____ ___ Directional gyro

_____ ___ Clock

_____ ____Vacuum gauge, if vacuum powered, or volt and amp meter, if electric

_____ ___ Heated Pitot

_____ ___ Generator or alternator

_____ ___ Alternate Static Source

_____ ____Altimeter and Static System as well as Transponder checks

Electrical Systems

Wire type and size is appropriate for load being carried, and connections are solid. All installed systems perform as intended.

Electrical

____ _____ Battery & Electrical System, wiring adequate size and secure

____ _____ Switches marked for operation, and wired properly

____ _____ Circuit Breakers or fuses labeled for value and function, and wired properly

____ _____ Ground on battery to airframe, or wired into place properly

____ _____ Ammeter

____ _____ Voltmeter

____ _____ Landing Lights / Position Lights wired correctly

____ _____ Cockpit lights/ Instrument lighting

____ _____ No interference between any electrical magnetic device and Compass

____ _____ Battery case and battery securely mounted

_____ ____ Battery vented overboard

Avionics

_____ _____ Antennas are properly installed, and have proper support/doubler plates

_____ _____ Coax Cable secured, with slack enough to prevent disconnection

_____ _____ Radios/Avionics and cooling fans are mounted securely

_____ _____ Avionics gear is wired properly, and functions

_____ _____ Transponder "Mode C" check done, and in aircraft records VFR vs IFR

Fuel System

_____ _____ Caps fit, and are vented on all tanks

_____ _____ Fuel drains installed at lowest portion of tank, and at lowest point in fuel lines

_____ _____ Fuel Vent System contains no loops which would block venting

_____ _____ Shutoff valve/ Selector switch ease of operation, and clearly marked for intended operation

_____ _____ Fuel control valve handle accessible in flight without loss of visual horizon or seat belt disconnects

_____ _____ Fuel Line routing proper material and diameter for intended fuel supply

_____ _____ Fuel Strainer functional and safety wired

_____ _____ Fuel Lines protected from chafing, and secure from "catching a foot."(Checklist explanations Page)

_____ _____ Fuel line routing avoids areas of heat

Gear/Wheel/Brake Systems

_____ _____ Retractable Gear functions- Operations check

_____ _____ Emergency gear extension test

_____ _____ Clearance in wheel wells

_____ _____ Brake System line routing, reservoir, pumps

_____ _____ Brake & Wheel installation secure

_____ _____ Brake pads properly conditioned

_____ _____ Taxi test on gear toe in/ toe out o.k.

_____ _____ Tires are clear of pants or struts, including clearance of "mud scraper", no binding

_____ _____ Wheel Pants are secure

_____ _____ Tail Spring secure, well designed, and is clear of rudder, steering linkage secure

Control Surfaces

A. Designers Recommended limits:

This Plane Measures:

Aileron Up travel: ______ Degrees/Inches _______ Degrees/Inches

Down travel : ______ Degrees/Inches _______ Degrees/Inches

Elevator Up travel: ______ Degrees/Inches _______ Degrees/Inches

Down travel: ______ Degrees/Inches _______ Degrees/Inches

Rudder Left/Right ______ Degrees/Inches _______ Left       _______ Right

General Condition- Fuselage, Wing, Tail Assembly

_____ _____ Skin condition, wrinkles, rivets, or tape

_____ _____ Vertical Fin, movement and condition

_____ _____ Elevator assembly, movement and condition

_____ _____ Trim Tabs function, no binding, heavy structure to reduce flutter potential

_____ _____ Control Travel "Stops"

_____ _____ Control Cables Safety Wired Correctly

_____ _____ Counterweights secure

_____ _____ Doors close securely and open properly, if open in flight, markings

_____ _____ Emergency external access and markings

_____ _____ Windows secure, and markings for distance if open in flight

_____ _____ Canopy secure

_____ _____ Canopy emergency release marked red and copper safety wired

_____ _____ Canopy locks/door locks work

Flight Controls

_____ _____ Proper tension of cables

_____ _____ Safety wiring of cables

_____ _____ Clearance on controls/no hitting panel or floorboards

_____ _____ Control System Stops

_____ _____ Freedom of movement

_____ _____ PROPER DIRECTION

_____ _____ Is everything safetied?

Engine Compartment

_____ _____ Engine Compression in Logs1=___ 2=____ 3=____ 4=____ 5=____ 6=___

_____ _____ Throttle cables anchored and functional, spring open travel cushion

_____ _____ Clearances in engine compartment

_____ _____ Carb Heat Control- Functional Travel Cushion

_____ _____ Mixture Control- Functional, spring full-rich Travel Cushion

_____ _____ Fuel Hose routing to avoid heat & bends (Fire sleeve preferred)

_____ _____ Engine fluid hoses inspected for obstructions and debris, cleaned before installation

_____ _____ Fuel strainer safety wired

_____ _____ Fuel Hose diameter sufficient for engine

_____ _____ Fuel and Oil Hoses proper material

_____ _____ Oil System Hose & Cooler installation

_____ _____ Prop Governor. Functional, proper lines stops adjusted

_____ _____ Firewall steel, no openings

_____ _____ Engine Mount secure, no cracks

_____ _____ Alternator, belts, accessories properly installed

_____ _____ Heater hoses proper material

_____ _____ Heater design minimizes CO poisoning chances

_____ _____ Baffles appear correct

_____ _____ All electrical and ignition wires appear correct

_____ _____ Cowling secure.

Propeller

_____ _____ Propeller nicks

_____ _____ Safety Wired Bolts of sufficient size

_____ _____ Bolts torqued properly

_____ _____ Bolts clear engine, proper length

_____ _____ Prop clears ground in takeoff attitude by >7"

_____ _____ Propeller tips track OK

_____ _____ Prop Spinner o.k., clear of cowl, not uneven spin

_____ _____ Ready for Run-up.

Test Run Engine

Note: At least one hour of run-up should be considered when approved by engine manufactures and approved re-builders procedures, and logged in the aircraft logbook. The engine compressions should also be recorded after one Hour of run-up. Some may be low on a fresh overhaul engine, but it is important to get this information as a base line! Common practice is not to run a freshly overhauled engine that has not had a test cell ground run.

_____ _____ Engine starts easily

_____ _____ Oil Pressure comes up quickly to proper level

_____ _____ Oil Temp comes off cold peg

_____ _____ Check all instrument operations/tach/oil/volts/ etc.

Record all data five minutes after startup here _________

_____ _____ Carb Heat Functions, RPM Drop is ________

_____ _____ Mag Drop, Left is ______ Right is _______

_____ _____ Fuel Gauges show calibrated

_____ _____ Mixture/Throttle/Prop controls work

_____ _____ Fuel Shutoff works

_____ _____ No abnormal vibration

_____ _____ Propeller tracks within specs

_____ _____ Idle cut off produces slight RPM rise when operated for engine shutdown

Airworthiness Directive Compliance

____ ______ Engine AD's which apply have been complied with, and how (Attach list if necessary)

__________________________________________________________________________________________

_____ ______ Equipment AD's which apply have been complied with, and how (Attach list if necessary)

__________________________________________________________________________________________

Certification

_____ ______ Logs present and builder records the following statement:

I certify that I have built this aircraft for my own education and recreation, and I have inspected it fully. I am the manufacturer, and I consider it eligible for issuance of an Experimental Airworthiness Certificate for the purpose of operating amateur-built aircraft under provisions of FAR 21.191(g).

_____ _______Discuss operating limitations with applicant, flight test areas, and flight test time.

_____ ______ Airworthiness application properly filled out and signed?

_____ ______Sign Logbook and issue certificate, if applicable.

OR

______ ______Provide list of deficiencies to applicant, if applicable

Unsatisfactory Conditions

N_______ Owner __________

The following unsatisfactory conditions were noted in your inspection. It is your responsibility to correct these conditions prior to obtaining an airworthiness certificate. Please correct the deficiencies and return this list, with evidence of the corrections, to the certificating inspector.

1. Condition:______________________________________________

Corrective action taken: ___________________________________

________________________________________________________

2. Condition: ____________________________________________

Corrective action taken: _______________________________________________________

Signed: _________________________